ST. MARGARET ENGINEERING COLLEGE

PAPER PRESENTATION ABSTRACT

TOPIC: RED TACTON (H.A.N Technology)

PARITICIPANTS: Deepanshu Sharma (07EC017) , Rahul kr.Garg (07EC060).

OVERVIEW:

“RedTacton” gives the whole new meaning to the term “Networking”.

Red Tacton is a new personal area networking technology which uses the surface of the human body as the safe data transmission path. The speed of the data transmission is up to 10Mbps. Red Tacton uses a weak electric field on the surface of the human body for data transmission. The Red Tacton chips, contains a transmitter and receiver to send and accept data in digital format.

Red Tacton is the Future of wireless communications. Red Tacton is also called as Human Area Networking Technology.The data is transferred by the human body surface like hands, legs etc. and it is also possible through clothes and shoes also.

WORKING:

The Red Tacton transmitter consists of a transmitter circuit including electric field on the human body. And the data sense circuit also includes in the transmitter circuit. This data sense circuit distinguishes transmitting and receiving modes by output control signals of these two modes.

The receiver consists of an electro optic sensor and a detector circuit. The detector circuit amplifies the signal from the electro optic sensor and converts it in to electrical signal.

Red Tacton has basically three features:

1. Touch

2. Broadband and Interactive

3. Media

Application of Red Tacton :

• Communications between devices on the same person. (No cord between the earphones and device, Elimination of Human Error)

• Communication between devices on different persons. (Exchange electronic business cards by shaking hands)

•  Communication from a device on a person to the device embedded in the environment. (Authentication is performed by reading the ID when we walk   through the gate, Security Applications)

•  Communication from a device embedded in the environment to a device on a person, (Here music or description by standing in front of an exhibit)

•   Communication between the devices mediated by the conductor in the conference system.

This technology definitely stands out with perfection, when transfer of data is fast, feasible and more importantly reliable. So, in few years from now everything is going to fall under this super technology. And, finally I conclude that

“FUTURE BELONGS TO RED TACTON”